## Slide 1: internet

## Slide 2: alapconfig
Username cisco secret cisco
Line vty 0 15
  Login local
  Transport input ssh
Ip domain name R1.karacs.hu
Ena secret cisco
Hostname R1
Crypto key generate rsa(2048)
Router ospf 1
  Router-id 1.1.1.1

## Slide 3: Lan interface
interface GigabitEthernet0/0/1
ip address 192.168.4.1 255.255.255.0
ip nat inside
Ip ospf 1 area 0
negotiation auto

## Slide 4: Serial
ip address 192.168.5.2 255.255.255.252
ip nat inside
ip ospf 1 area 0

## Slide 5: Wan interface
interface GigabitEthernet0/0/0
ip address dhcp
ip nat outside
Ip ospf 1 area 0
negotiation auto

## Slide 6: Nat + ip route
ip access-list standard 1
10 permit 192.168.3.0 0.0.0.255
20 permit 192.168.4.0 0.0.0.255
ip nat pool MEDENCE 10.204.211.104 10.204.211.104 netmask 255.255.255.192
ip nat inside source list 1 pool MEDENCE overload
ip route 0.0.0.0 0.0.0.0 10.204.211.126

## Slide 7: R2
Username cisco secret cisco
Line vty 0 15
  Login local
  Transport input ssh
Ip domain name R2.karacs.hu
Ena secret cisco
Hostname R2
Crypto key generate rsa(2048)
Router ospf 1
  Router-id 2.2.2.2

## Slide 8: G0/0/1 és Se0/1/0
interface g0/0/1
ip address 192.168.4.1 255.255.255.0
ip ospf 1 area 0
negotiation auto
interface Serial0/1/0
ip address 192.168.5.1 255.255.255.252
ip ospf 1 area 0

## Slide 9: Ip route
ip route 0.0.0.0 0.0.0.0 10.204.211.104